## Slide 1
Investigation of EBW current drive in open magnetic flux surface using flux loop with HFS injection in QUEST
ZHOU Junyaoa, HANADA Kazuakib, KOJIMA Shinichiroc, KONO Kaorib, IDO Takeshib, EJIRI Akirad, ONCHI Takumib, SEKIYA Izumib, KURODA Kengohb, YUE Qilina,
IDEI Hiroshib, NAGASHIMA Yoshihikob, IKEZOE Ryuyab, HASEGAWA Makotob, HIGASHIJIMA Akib, SHIMABUKURO Shunb
aIGSES, Kyushu University, bRIAM, Kyushu University, cQST, dGSFS, The University of Tokyo

## Slide 2: Review of X-B mode conversion experiments
Non-inductive current was driven by EBW after plasma current was started up, and the perpendicularly injected X-mode wave showed the most efficient EBWH/EBWCD.
https://doi.org/10.1103/PhysRevLett.89.265005
Reflection mirror was installed on center stack to reflect the X-mode wave from LFS.
The purity of reflected X-mode wave is difficult to confirm.
Installing antenna on the HFS is quite difficult.
8.2GHz RF system in QUEST.
A larger reflection mirror is necessary.
HFS injection system is possible.
2
COMPASS-D
Shevchenko V, 2002, PRL 89(26): 265005.
EBW assisted plasma current start-up was demonstrated for the first time in a tokamak.
17kA non-inductive plasma current was obtained by a 100kW RF power injected, and 33kA plasma current was achieved with optimized vertical field ramps.
Plasma current driven by EBW was proved according to the anti-phase response of to the vertical modulation of plasma mid-plane by changing PF coil current during RF injection.
MAST
Shevchenko V F, 2015, EDP Sciences 87: 02007.
Shevchenko V F, 2010, NF 50(2): 022004.

## Slide 3: HFS injection system in QUEST
Two klystrons with 25kW power output each were employed.
gas was filled in waveguide to avoid arcing on ECRL.
Incident antennas were located 0.17m above the equatorial plane.
Tungsten covers were used to protect the antenna from plasma.
PF1-7 and PF2-6 were employed to make a vertical magnetic field, , with n-index >0.3.
HCU and HCL coils were used to adjust horizontal magnetic field, , to eliminate the error field and shift plasma in vertical direction.
3
https://doi.org/10.1088/1361-6587/ab6903
PF2
PF1
PF7
PF6
HCU
HCL

## Slide 4: EBWCD couldn’t be clarified by measuring under different
Kojima S, 2021 [D]
An over-dense plasma which exceeded the plasma cutoff density ( was successfully excited using HFS injection.
HFS injection at 21 msec LFS injection at 21 msec
HFS injection at 121 msec LFS injection at 121 msec
A plasma current over 4kA was obtained by HFS injection. The jump of plasma current indicated the formation of CFS in both [] CW and [] CCW condition. However, the EBWCD was not clarified by reversing the direction of toroidal field or poloidal field coil current.
on negative PF & positive TF on negative PF & negative TF
on positive PF & positive TF on positive PF & negative TF
https://doi.org/10.1585/pfr.14.1205038
https://doi.org/10.1088/1361-6587/ab6903
4

## Slide 5: Object
Plasma start-up by a fully non-inductive current drive using X-B mode conversion from HFS injection was conducted in QUEST tokamak. A horizontal magnetic field was applied to eliminate the error field caused by the junction of toroidal field coils to make sure the plasma mid-plane was at the position of equatorial plane of vessel in both [] CW and [] CCW condition.
Direction of toroidal magnetic field was inversed in experiments while was not changed in order to distinguish the EBWCD and pressure driven current. The difference of EBWCD due to the inversing was expected to be reflected by the measurement of magnetic flux. The pressure driven current was estimated by the measurement of Thomson Scattering.
was further adjusted in the range of ±0.09kA to shift plasma in vertical direction. and were both inversed in this stage to investigate the effect of EBWCD on the formation of CFS under different magnetic field configuration.
5

## Slide 6: Measurements
Thomson scattering was employed to measure the electron density and temperature of 6 points (R=0.419m, 0.558m, 0.691m, 0.805m, 0.915m, 1.005m) on equatorial plane of vessel.
Interferometer was used to measure the line-integrated electron density.
24 flux loop coils were distributed longitudinally every 0.1m on the center stack to measure the vertical magnetic flux generated by plasma current.
0.0
1.0
1.5
2.0
-2.0
-1.5
-1.0
-0.5
0.0
0.5
1.0
1.5
2.0
0.5
FLC1~24
6
https://doi.org/10.1585/pfr.15.2402063
https://www.triam.kyushu-u.ac.jp/community/

## Slide 7: Inversing for changing the direction of BWCD
& was applied respectively to eliminate the error field
Negative range: inward to center stack
Positive range: outward to center stack
White line: plasma mid-plane
[] CW [] up
#48532
1.0
0.5
0.0
-0.5
-1.0
Z [m]
R [m]
0.0
0.4
0.6
0.8
1.0
[T] in R-Z plane
Anti-equilibrium
Equilibrium
0.2
direction was inversed to distinguish the EBWCD from pressure driven current.
7
[] CCW [] up
Z [m]
[T] in R-Z plane
R [m]
0.0
0.2
0.6
0.8
1.0
1.0
0.5
0.0
-0.5
-1.0
Anti-equilibrium
Equilibrium
#48480
0.4

## Slide 8: Peak of magnetic flux moved by inversing
RF was launched from 5.0s to 5.22s. AM of RF power was conducted from 5.1s. CFS was successfully formed and the plasma current with a maximum over 4.9kA was obtained.
The peak changed to locate in the bottom half when direction was inversed to CW. It indicates that the main part of the equilibrium plasma current was driven by EBWCD.
The over-dense plasma was excited in both [] CCW and [] CW condition.
The pressure driven current was roughly estimated under the assumption that was same in [] CW and [] CCW condition.
5.01s
Plasma cutoff ()
ECRL
R=0.465m
8
Peak of driven current

## Slide 9: EBWCD with opposite directions in [] CW and [] CCW conditions
#48532
1.0
0.5
0.0
-0.5
-1.0
Z [m]
R [m]
0.0
0.4
0.6
0.8
1.0
Anti-equilibrium
Equilibrium
0.2
9
EBWCD [CW]
EBWCD [CCW]
Z [m]
R [m]
0.0
0.2
0.6
0.8
1.0
1.0
0.5
0.0
-0.5
-1.0
Anti-equilibrium
Equilibrium
#48480
0.4
Center Stack
ECRL
Direction of
EBWCD in CW
EBWCD in CCW
Center Stack
ECRL
Direction of
EBWCD in CW
EBWCD in CCW
[ ] CW
[ ] CCW
EBWCD [CCW]
EBWCD [CW]
Ion drift direction
Ion drift direction

## Slide 10: Plasma current behavior in OFS depending on magnetic field configuration
Almost constant in OFS, then jumped suddenly to the maximum.
[] CCW
Gradually increased in OFS until the maximum.
[] CW
The plasma current showed different behavior in OFS.
Plasma up-shift
Plasma failed to start-up
The plasma current growth rate showed negative in [] CCW condition.
The plasma current growth rate increased when the increasing for plasma up-shift was applied in both [] down and [] up condition.
The same trend couldn’t be observed clearly in [] CCW condition.
10
R [m]
0.0
0.4
0.6
0.8
1.0
0.2
1.0
0.5
0.0
-0.5
-1.0
Z [m]
0.05kA
0.07kA
0.09kA
Equilibrium
Anti-equilibrium
-0.09kA
-0.07kA
-0.05kA
-0.02kA
-0.00kA
0.02kA
R [m]
0.0
0.4
0.6
0.8
1.0
0.2
1.0
0.5
0.0
-0.5
-1.0
Z [m]
Anti-equilibrium
Equilibrium

## Slide 11: Conclusions
11
The direction was inversed from CCW to CW in order to distinguish the EBWCD whose direction is depending on from pressure driven current whose direction is depending on . The peak of measured vertical magnetic flux at center stack located at top or bottom half of vacuum vessel depending on the direction of , which indicated that a part of equilibrium plasma current was driven by EBWCD.
The magnetic flux generated by pressure driven current was roughly estimated because the magnetic configuration was same except the direction of when error field was eliminated by applying . Then EBWCD in [] CCW and [] CW condition was estimated. The results indicated that directions of EBWCD on two sides of plasma mid-plane show similar magnitude and opposition direction. Consequently, the peak of driven current appeared at top or bottom half due to the anti-equilibrium or equilibrium case.
Plasma current in OFS showed constant in [] CCW condition and showed ramp-up behavior in [] CW condition. was adjusted in range of ±0.09kA to further investigate the effect of EBWCD on the formation of CFS. The plasma current grew faster in OFS when larger for plasma up-shift was applied because the equilibrium zone was expanded. Oppositely, when anti-equilibrium zone was expanded, the CFS failed to form. It indicated that EBWCD contributed to the plasma start-up and played an important role in the formation of CFS. However, the same conclusion couldn’t be obtained in [] CCW condition. It will be discussed in future work.