## Slide 1: Development of full electromagnetic plasma start-up model for analysis and prediction of Ohmic discharges in Versatile Experiment Spherical Torus
Seongcheol Kim1, Hongsik Yun1, Hyun-Tae Kim2, Jae Young Jang1,3, Jung-Hwa Kim1, TaeHee Eom1 and Y. S. Hwang1
1Department of Nuclear Engineering, Seoul National University, Korea
2United Kingdom Atomic Energy Authority, Culham Science Centre, United Kingdom of Great Britain and Northern Ireland
3Korea Institute of Fusion Energy, Daejeon, Korea
ISTW 2022 (Monday, Oct. 31 – Friday, Nov. 4)
The 21st International Spherical Torus Workshop

## Slide 2
1. Introduction
2. Plasma current ramp-up phase
3. Plasma burn-through phase
4. Reproduction of two Ohmic discharges with different loop voltage using reduced start-up model
5. Summary and Future works
Contents

## Slide 3
1. Introduction
1.1. Background & Motivation
1.2. Research objectives

## Slide 4
1. Introduction
1.1. Background & Motivation
Hydrogen-α
Plasma current
Tokamak start-up diagram
Loop
voltage
Plasma
breakdown
Plasma
burn-through
IP ramp-up
    1) Classical Townsend breakdown
  2) Plasma burn-through
    Full ionization of Hydrogen and low-Z impurities (Carbon and Oxygen)
    Ionization and radiation losses
    Necessary to heat the plasma for IP ramp-up
  3) Subsequent current rise of IP
    Increasing Te for IP ramp-up due to RPTe-1.5
Prefill neutral pressure
Feedback control
https://step.ukaea.uk/
https://www.iter.org/
1) Use of superconducting magnets for PF coils
2) Thick vacuum vessel
 Limited toroidal electric field ~0.3 V/m
Fusion reactor based on spherical tokamak
 Restriction of central solenoid coil space in center stack
ITER
STEP
Start-up issues in future fusion devices
Necessity of reliable tokamak start-up modelling
Operation scenarios for successful start-up
Design parameters in a new device
[Nucl. Fusion 39 (1999) 2577]

## Slide 5
1. Introduction
1.2. Research objectives
VEST
Development of start-up model with DYON
Compact ST devices
Spherical torus plasma
Short pulse discharges (< 30ms)
Validation diagnostics targeted to relatively low performance plasmas
Reproduction and analysis of start-up in VEST discharges
Application to the
VEST-U for ~300 kA OH discharge
Research objectives: overall structure
Interpretative
Predictive
DYON
Zero dimensional burn-through simulator (particle + power balance & circuit model)
Dedicated physical model (atomic, confinement, PSI, ECH models)
Experimentally validated at several machines (JET & MAST)
Electromagnetic effect transport effect
 Utilization of DYON to whole discharge model in VEST
Model development for extension of utility
Focus on the plasma burn-through and current ramp-up phases
Nucl. Fusion 52 (2012) 103016
Nucl. Fusion 53 (2013) 083024

## Slide 6
2. Plasma current ramp-up phases
2.1. Magnetic equilibrium reconstruction
2.2. Electric circuit parameters in circuit model
2.3. Target discharge and simulation results

## Slide 7
2. Plasma current ramp-up phases
2.1. Magnetic equilibrium reconstruction
Evolution of plasma current
  Circuit model:
  Prescribed circuit parameters: external inductance (), internal inductance (), plasma resistance ()  Largely dependent on plasma shapes
  Important for reliable plasma shape from equilibrium reconstruction
  Equilibrium reconstruction in VEST
    Typical EFIT-like Grad-Shafranov solver with external magnetics constraints
    Eddy current model with effective wall resistance compensation
Measurements
Synthetic (before Rw compens.)
Synthetic (after Rw compens.)
Time (ms)
Bz (mT)

## Slide 8
2. Plasma current ramp-up phases
2.2. Electric circuit parameters in circuit model
Plasma external inductance model
Typical A range in ST
Comparison of plasma external inductance with A between two models
High-A model
High aspect ratio Le model (previous DYON model)
 Dependent of plasma shape parameters ()
Pegasus
VEST

## Slide 9
2. Plasma current ramp-up phases
2.2. Electric circuit parameters in circuit model
Plasma external inductance model
High-A model vs Hirshman model
High aspect ratio Le model (previous DYON model)
Low aspect ratio Le model derived by Hirshman [Ref]
 Dependent of plasma shape parameters (, )
Typical A range in ST
Comparison of plasma external inductance with A between two models
where ,
Pegasus
VEST
[Phys. of Fluids 29 (1986) 790]

## Slide 10
2. Plasma current ramp-up phases
2.2. Electric circuit parameters in circuit model
Plasma external inductance model
where ,
High aspect ratio Le model (previous DYON model)
 Dependent of plasma shape parameters (, )
Modified Le model using VEST equilibrium
Typical A range in ST
Comparison of plasma external inductance with A between two models
High-A model vs Hirshman model
Low aspect ratio Le model derived by Hirshman [Ref]
Pegasus
VEST
[Nucl. Fusion 58 (2018) 076011]

## Slide 11
Plasma resistance model
  Classical spitzer resistivity model
    Other factors?
      Neoclassical enhancement resistivity?
        Significant trapped particle fraction in ST plasmas
        Analytic model for neoclassical enhancement factor
          Trapped particle fraction [Phys. Fluids B 4 (1992) 4023]
          Neoclassical factor [Phys. of Plasmas 6 (1999) 2834]
        Parameters required for neoclassical factor can be obtained self-consistently in the model
          Plasma shape parameters  prescribed
           particle and power balance model
           function of
2. Plasma current ramp-up phases
2.2. Electric circuit parameters in circuit model
Prescribed plasma shapes
Self-consistently obtained by power & particle balance models

## Slide 12
2. Plasma current ramp-up phases
2.3. Target discharge and simulation results
Target discharge and validation diagnostics
Typical pure Ohmic discharge in VEST (Shot#37430)
  Toroidal field at R~0.4 m: 0.18 T
  Neutral prefill pressure (H2): 0.04-0.05 mTorr
  Validation diagnostics
Laser system
Thomson scattering (Te, Ne)
Ion Doppler spectroscopy (Ti)
Optical filterscope (Hα, CIII)
Line of sight 0.39 – 0.71 m
(Only using 0.39 m)
Toroidal view
Polychromator + Fast digitizer
TS local points
0.475, 0.425, 0.37, 0.31, 0.255 m

## Slide 13
2. Plasma current ramp-up phases
2.3. Target discharge and simulation results
Start-up model results
Measurements
Model (High-A Le, VEST Le, VEST Le & neo-factor)
Extremely high and fast evolution especially in IP and Te compared to measurements with high-A Le model due to the low external inductance
Invalid in low aspect ratio plasmas
Relaxed evolution parameters compared to those of High-A Le results due to reduced plasma inductance
Difficult to simulate the degradation of IP observed in the measurement
IP degradation
Reasonable agreements by considering neoclassical enhancement factor

## Slide 14
3. Plasma burn-through phases
3.1. Townsend model with full electromagnetic simulation
3.2. Preliminary results with Townsend model

## Slide 15
3. Plasma current ramp-up phases
3.1. Townsend model with full electromagnetic simulation
Full electromagnetic model
  To consider a realistic situation with PF coil and vacuum vessel wall structure in a specific device
  Electric circuit equation with matrix form for all vacuum vessel, PF coil elements and plasma current
Load PF & wall geometry, generate circuit matrix
Load PF coil current waveform
Synthetic flux loop data
Validation of electromagnetic model of DYON in vacuum discharge of VEST
[Shot#34497]
Solving
Circuit eqs.
v: vessel
c: PF coil
p: plasma
PF #01
PF #05
PF #06
PF #09-PF #10
Flux loops
[Nucl. Fusion 62 (2022) 126012]

## Slide 16
Townsend model
  To identify plasma volume at early burn-through phase
  Townsend breakdown voltage,
    Where p is a neutral pressure and Lf is a connection length
3. Plasma current ramp-up phases
3.1. Townsend model with full electromagnetic simulation
2D poloidal magnetic configuration from the electromagnetic model,
Averaged parallel electric field parallel with field following method, using
To determine the Townsend criteria by comparing
to the
To gather all grid points which satisfies the Townsend criteria,
and to estimate plasma volume
[Nucl. Fusion 62 (2022) 126012]

## Slide 17
3. Plasma current ramp-up phases
3.2. Townsend model with full electromagnetic simulation
Model results with finite element current distribution vs point source
Magnetic flux evolutions
Finite element current distribution
Single point source current

## Slide 18
3. Plasma current ramp-up phases
3.2. Townsend model with full electromagnetic simulation
Magnetic flux evolutions
Finite element current distribution
Single point source current
Model results with finite element current distribution vs point source

## Slide 19
4. Reproduction of two Ohmic discharges
with different loop voltage using the reduced startup model
4.1. High current with short pulse and Low current with long pulse Ohmic discharges
4.2. Prefill neutral pressure and Loop voltage scanning

## Slide 20
4. Validation of Ohmic discharges with reduced model
4.1. High IP with short pulse and Low IP with long pulse OHs
Ohmic discharges with different loop voltage waveforms
Shot#32315: High IP with short pulse
Shot#32302: Low IP with long pulse
Operation conditions & feature of two discharges
 | High IP with short pulse | Low IP with long pulse
Toroidal field (T) | 0.174 | 
Operating pressure (mTorr) | 0.015 | 0.005
Wall condition method | HeGDC with boronization | 
Loop voltage | Left figure | Left figure
Plasma size | R0~0.43 m and κ~2 | R0~0.35 - 0.4 m and κ~1.75
Hα signal | No clear burn-through peak due to the significant H recycling | 
Mirnov signal | Strong | Weak
OKAY

## Slide 21
4. Validation of Ohmic discharges with reduced model
4.1. High IP with short pulse and Low IP with long pulse OHs
High IP with short pulse
Low IP with long pulse
Discrepancy in Ha emission signal between measurement and model
Reproduction of plasma current evolution with reasonable agreements
Quantitative validation of Te & ne evolution in future Ohmic discharges

## Slide 22
4. Validation of Ohmic discharges with reduced model
4.2. Prefill neutral pressure and loop voltage scanning
Experiment set-up
 | Scanning experiments (1) | Scanning experiments (2)
Adjustment parameters | Prefill neutral pressure Equilibrium field | Loop voltage by central solenoid Equilibrium field
Fixed parameters | Loop voltage by central solenoid Toroidal magnetic field | Prefill neutral pressure Toroidal magnetic field
Simulation results with statistical comparison

## Slide 23
5. Summary and Future works

## Slide 24
5. Summary and Future works
Summary
  Improvements of circuit parameter models (Le for low-A plasmas and neoclassical factor) for reliable plasma current evolution
  Development of Townsend breakdown model with coupled a full electromagnetic model in order to estimate the plasma volume
  Reproduction of an elongated ST plasma (IP, Te, ne, Ti, Hα, CIII and plasma shape) with reasonable agreements using the full electromagnetic model
  Statistical validation of the startup model (w/o electromagnetic model) with different prefill neutral and loop voltage parameters
Future works
  Experimental validation of Townsend breakdown model
    Plasma volume estimation using fast camera images and electrostatic probe
  Reproduction of Ohmic start-up with various operating conditions using full electromagnetic start-up model
  Prediction of VEST-Upgrade Ohmic discharge

## Slide 25
1. Introduction
1.2. Research objectives
DYON simulator
Power balance, particle balance & circuit equation

## Slide 26
4. Parameters scanning experiments and simulation results
4.1. Boronization wall condition effect in VEST
Ohmic discharge w/o boronization coating
Ohmic discharge with boronization coating
Neutral pressure decrease when burn-through
Clear hydrogen burn-through peak
Uncertain hydrogen
burn-through peak
Neutral pressure increase due to the severe H retention during boronization GDC

## Slide 28
4. Validation of Ohmic discharges with reduced model
4.1. High IP with short pulse and Low IP with long pulse OHs
High IP with short pulse
Low IP with long pulse
Difficult to simulate the unclear hydrogen burn through peak observed in experiments

## Slide 29
4. Validation of Ohmic discharges with reduced model
4.2. Neutral pressure scanning
0.038 mTorr O  O
0.047 mTorr O  O
0.055 mTorr O  O
Lagging why??

## Slide 30
4. Validation of Ohmic discharges with reduced model
4.2. Neutral pressure scanning
0.061 mTorr O  X
0.073 mTorr X  X
Case4 (0.061 mTorr)
Experiments: burn-through ok
Model: burn-through fail
Other cases are consistent

## Slide 31
4. Validation of Ohmic discharges with reduced model
4.2. Loop voltage scanning
Loop voltage1 O  O
Loop voltage2 O  O
Loop voltage3 O  O

## Slide 32
4. Validation of Ohmic discharges with reduced model
4.2. Loop voltage scanning
Loop voltage4 O  X
Loop voltage5 X  X
Case4
Experiments: burn-through ok
Model: burn-through fail
Other cases are consistent

## Slide 33
4. Validation of Ohmic discharges with reduced model
4.2. Volume averaged value
Necessity
Electron temperature and density by Thomson scattering are local measurements
For comparison with DYON calculation, volume averaged quantities are needed
Te and Ne from TS and flux information from equilibrium reconstruction are needed
Processing
  TS scattering data mapping at flux coordinates by using eq. data
  Interpolation of Ne, Te data in real dimension (R,Z)
  Calculation of volume averaged quantities
Upper limit
Lower limit
Shot#37441 @ 307 ms
R (m)
R (m)